## Slide 1: Hybrid P2P LAN communication application
INTRODUCTION
ABSTRACT
ECEN 401 :: Dr. Bassem Mahmoud Mokhtar By :: Gad Mohamed
In LAN networks we don't need internet to reach each, we can communicate with higher speeds. A hybrid communication application on LAN is described and implemented. In hybrid application, clients are not only independent from server's central authority, but they can also depend each other to acquire services in case they can't afford to obtain it themselves. This is useful for devices that are connected on a local network where high-speed communication is possible without the need for internet access
NUchat provides many services like network and port scanning, messaging, file sharing, authentication via NU email, encryption of messages, and delivers all these capabilities in a friendly user interface. There is no code for server and another for client, the application has only one GUI and every client is capable of gathering the information he needs to find, reach, and communicate with other clients in the network. If the client can't obtain any of these services, the application implicitly asks other clients to share the information they've gathered. The first step is to scan the network using ARP protocol with each possible IP in the identified subnet mask, then the ports that the application uses are scanned in all the obtained IP addresses to identify devices that have this application running, the results are shown to the user, so he can choose one of the clients to communicate with. Just like DNS server works, each user can authenticate his identity to others using NU email so that other user can see his email instead of seeing his IP. After connection is established between two users they can chat or share files. Chatting is secured by encrypting messages.
Discussion and conclusion
Hybrid applications are efficient in that they don't rely on a central server. While pure P2P architecture are characterized by their fully decentralized nature, hybrid architecture introduce a combination of both server based and P2P systems to give the chance and provide services for clients who're not capable of maintaining these services by themselves.
References
Mahdi Ebrahimi, Mohammad A. Bazyar (2008). Benefiting from Data Mining techniques in a Hybrid Peer-to-Peer Network. International Conference on Advanced Computer Theory and Engineering
Future work & Suggestions
New features might be added like VOIP service.
Results
IP: XX:XX:XX:XX
Port 35000? NO
Port 7070? NO
IP: XX:XX:XX:XX
Port 35000? YES
Port 7070? YES
Connection established
Between XX:XX:XX:XX
And XX@nu.edu.eg
IP: XX:XX:XX:XX
Port 35000? NO
Port 7070? NO
IP: XX@nu.edu.eg
Port 35000? YES
Port 7070? YES
IP: XX:XX:XX:XX
Port 35000? YES
Port 7070? YES
Connection established
Between XX:XX:XX:XX
And XX@nu.edu.eg
IP: XX@nu.edu.eg
Port 35000? YES
Port 7070? YES
METHODOLOGY
P2P process flow
SERVER-CLIENT process flow
An incapable user reaches another user and asks for his search list.
A user can also ask another user to authenticate his identity and broadcast confirmation to other users
Authentication request
User 1 scanning again
and sees User 2 identity
User 1 scanning
User 2 authenticating himself
User 2 captured by his IP
User 2 captured by his NU email
Time cost for IP scanning for
class A VS class B
Time cost for successful and failed
authentication trial (approximated)
Process flow time cost from scanning to chatting